## Slide 1: Planet signal extraction from direct imaging using common spatial pattern filtering
J. Shapiro, N. Ranganathan, D. Savransky, J.B. Ruffio, B. Macintosh, and the GPIES Team
August 10, 2017
Paper 10400-56
Notes: Good afternoon, and thank you for being here today. I’m going to talk about a new method to aid in detecting exoplanets from direct imaging: common spatial pattern Filtering.
But first, let’s look at the very basics: direct imaging.

## Slide 2: Direct Imaging Standards
Exoplanet imaging is difficult:
  Faint signal
  Significant noise
The Current Standard: Principal Component Analysis (PCA)(Wold, 1987)
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
β Pic, GPIES Nov 2015
Notes: Direct Imaging, as many of you may know, is the science of detecting exoplanets by observing them and blocking out the parent star. Many of you also know that this is not easy. While a coronagraph blocks the majority of the stellar light, the noise in the images nearly completely obscures the planet signal, so extracting it is difficult.
One example is a current technique for doing this. Go from an image on the left, to one on the right, where the yellow dot is a clear planet signal.

## Slide 3: PCA and Common Spatial Patterns(Wang,2005)
Angular Differential Imaging(Marois, 2006)
PCA:
  Subtracting a least-squares approximation of an image from the image itself
  Karhunen-Loève Image Processing (KLIP)(Soummer, 2012)
CSP:
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Jessica Donaldson
astrobites, 2013
Notes: How do we get the transition from the previous slide? The core of KLIP, and the new process I will be describing today. For KLIP, let X be a distribution of images from a set of observations, and we find a new set of basis vectors to visualize the image. In the new basis vectors,
If you compare the two, there’s a very similar approach, but fundamentally different question. And that question is, what are the major differences between two data sets?

## Slide 4: Problem Definition
Let X1 be all the images from one observing sequence
Let X2 be the same data, derotated
Columns of Xn are single vectorized images
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: If we set up X1 and X2 like this, where X2 is the same dataset, but derotated, the movement of the planets is a PART of that answer.

## Slide 5: Solving
Composite Covariance Eigenvalue Decomposition
Whitening Matrix
Whitened, Normalized Data
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
.

## Slide 6: Solving
Composite Covariance Eigenvalue Decomposition
Whitening Matrix
Whitened, Normalized Data
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
.

## Slide 7: Solving
Reformulation
Solution
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
...
Notes: The w’s that solve the optimization, the initial question, are the eigenvectors of the whitened covariance matrix.
and share common eigenvectors.
The eigenvectors with the largest eigenvalues for have the smallest eigenvalues for . These correspond to eigenvectors that contain more information describing rather than
.
The w’s that solve the optimization, the initial question, are the eigenvectors of the whitened covariance matrix.
𝑆 ̂_1 and 𝑆 ̂_2 share common eigenvectors.
The eigenvectors with the largest eigenvalues for 𝑆 ̂_1 have the smallest eigenvalues for 𝑆 ̂_2. These correspond to eigenvectors that contain more information describing 𝑋_1 rather than 𝑋_2.
𝛴_1+𝛴_2=𝐼.

## Slide 8: Extracting the Planet Signal
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Zk is final k rows from Z
Signal for a given target image t is
Notes: For Z, we know that the eigenvectors associated with the highest eigenvalues correspond to more information content, big modes of the images. The planetary movement exists on the opposite end of the spectrum, associated with the smallest eigenvalues. So, we select the final K rows.
For each target Image, derotate and stack.

## Slide 9: Extracting the Planet Signal
Zk is final k rows from Z
Signal for a given target image t is
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: And there you have it. It works. How well does it work? Well, the answer is…it depends. On a lot of things, but one of the key factors is the third line. How many modes of the system do we want to examine?

## Slide 10: Modes Overview
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Maximum Eigenvalue
Eigenvalue ~ 0.5
Minimum Eigenvalue
Original Image:
Notes: This is very straightforward data, true data is NEVER this clear.
So, these are 3 different modes in Z. The first is the maximum eigenvalue. The most information content in X1, but not in X2. middle is information content in both. Final is content that would explain X2 relative to X1. So…a planet signal moving from a derotated spot to it’s original.
The bottom ones all have a little bit of the planet signal. So how many do you select, and what happens if you get it wrong?

## Slide 11: Threshold – Too High, 0.05
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Background noise is strong

## Slide 12: Threshold – Too Low, 0.002
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Signal is VERY distorted

## Slide 13: Threshold – Just Right, 0.005
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Arc Length
  More area swept out needs more modes to capture the motion
Signal Strength
  Stronger signal requires more modes
With an unknown signal, thresholding will likely require iteration
These simple examples were with injected planets into very simple synthetic noise I generated. The whole problem becomes more complicated when you look at more complex data with different correlations. So that’s what I did next.

## Slide 14: Data Sources
GPIES, Nov 2015, β Pic b
Limited to ADI
Repeated analysis on HD 1466
Planetary Injection
  2D Gaussian fit to β Pic b
  Same strength as β Pic b
  Rotate with Parallactic Angle
  5 injected
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Gemini Planet Imager Exoplanet Survey Instrument at the Gemini Observatory in Chile.
Stayed within the same wavelength. HD 1466 as an arbitrary choice to confirm findings.
2D Gaussian is not exactly the PSF, but it’s an approximation I believe to be sufficient for this analysis
Each injected is 60 degrees apart, leaving room for the known planet signal. Didn’t want interference.

## Slide 15: Methodology
Angular Separation
  From inner ring to outer ring
  Measurements averaged at given radius
  Moving through noise regimes
Varied signal strength
  0.5 to 4.5 percent of max value
  Each set of 5 averaged together
Iterated through different thresholds
  Kept the strongest Signal-Noise Result
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: One of the variables I wanted to look at to evaluate performance. Here, the two superimposed images have greatly exaggerated signals to demonstrate my point

## Slide 16: Evaluation Metrics
Signal – Noise Ratio
Signal strength is peak of fit Gaussian
Noise area is local section of annulus
Astrometric Biases
Matched filter
Point of maximum cross-correlation
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion

## Slide 17: Signal to Noise Ratio
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Bars across I think are a result of needing finer fidelity in the thresholding. I iterated across fairly large jumps. .05 to 0.1 to .15. I think smaller movements for a more optimal threshold would avoid blanket discrepancies like that. Also, some of the really high ones are just where the algorithm could likely not detect a planet.

## Slide 18: Centroiding Error
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Bars across I think are a result of needing finer fidelity in the thresholding. I iterated across fairly large jumps. .05 to 0.1 to .15. I think smaller movements for a more optimal threshold would avoid blanket discrepancies like that. Also, some of the really high ones are just where the algorithm could likely not detect a planet.
These results fine on own, but really tell a story when compared with KLIP.

## Slide 19: CSP – KLIP Comparison, Beta Pic
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
SNR
Centroiding Error
Notes: Performs better closer to the IWA.
This is my own implementation of KLIP. Not quite as sophisticated as perhaps the GPIES data cruncher, but neither is the CSP method I’m testing. I suspect both are at similar levels of sophistication, which somewhat levels the playing field.

## Slide 20: CSP – KLIP SNR Comparison, HD 1466
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Confirms trends.

## Slide 21: Images (Left: CSP, Right: KLIP)
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Both find Beta Pic very well, and both mostly miss on the top 2 planets. CSP does a better job at identifying the bottom 2 and the one opposite from Beta Pic

## Slide 22: ROC Curve
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion
Notes: Both find Beta Pic very well, and both mostly miss on the top 2 planets. CSP does a better job at identifying the bottom 2 and the one opposite from Beta Pic

## Slide 23: Conclusions and Future Work
Common Spatial Pattern Filtering can be used to extract planet signals from direct imaging
Tentatively, CSP has higher SNR near inner working angle
Higher rate of false positives
Matched Filter
Validate on more star backgrounds
Develop procedure for SDI inclusion
Optimally sized regions
Introduction | Application | Mode Thresholding | Methodology | Results | Conclusion

## Slide 24: Acknowledgements
SIOSLab
  Dmitry Savransky
  Christian Delacroix
  Joyce Fang
  Daniel Garrett
  Dean Keithly
  Nikhil Ranganathan
  Amlan Sinha
  Gabriel Soto
The GPIES Team
Stanford Collaborators
  Bruce Macintosh
  J.B. Ruffio
This work is supported by NASA Grant No. NNX16AI13G.

## Slide 25: Planet signal extraction from direct imaging using common spatial pattern filtering
J. Shapiro, N. Ranganathan, D. Savransky, J.B. Ruffio, B. Macintosh, and the GPIES Team
Paper 10400-57
August 10, 2017
Paper 10400-56
Notes: Good afternoon, and thank you for being here today. I’m going to talk about a new method to aid in detecting exoplanets from direct imaging: common spatial pattern Filtering.
But first, let’s look at the very basics: direct imaging.